MEASUREMENT CHECKLIST

___   Do you have the exit slits you need in?

___   Do you have correct D1 & is it centered?

___   Have you checked the PHD on each EM?

___   Do you have correct ES & AS (probably at least ES3 & AS2)?

___   Is C4x aligned?

___   Have the following been optimized for highest MRP?
          ___   Q
          ___   LF4
          ___   Hex
          ___   Hx & Hy postition
          ___   Focal voltage (absolutely last)

___   Are secondary ions for each species aligned in vertical and horizontal?
          ___   If not, use Bvert & Bhor

___   Are secondary ions for each species aligned in EOS?
          ___   If not, use Bvert & Bhor

___   Have the following been maximized?
          ___   Cy
          ___   P2/P3
          ___   EOS
          ___   Energy